## Slide 1: CATALYSIS AND CATALYTIC REACTION MECHANISM PART 1

## Slide 2: CATALYST-DEFINITION
A catalyst is a substance that affects the rate of a reaction but emerges from the process unchanged.
A catalyst usually changes a reaction rate by promoting a different molecular path ("mechanism") for the reaction.
Catalyst affect yield and selectivity
Changes only the rate of reaction; it does not affect the equlibrium.

## Slide 3
ERT 208/4 REACTION ENGINEERING
SEM 2 (2009/2010)
Students should be able to;
DISCUSS the steps in a heterogeneous reaction
(adsorption, surface reaction, and desorption)
DESCRIBE the rate limiting step.
EXPLAIN different types of surface reaction (single
site, dual site, and Eley-Rideal)
ANALYZE data to DEVELOP a rate law for
Langmuir- Hinshelwood kinetics.

## Slide 4: Steps in Catalytic Reaction
External diffusion
Internal diffusion
Adsorption
Surface reaction
Desorption
Internal diffusion
External diffusion

## Slide 5
Steps in Catalytic Reaction
Mass transfer (diffusion) of the reactant from the bulk to the external transport.
Internal diffusion
Adsorption
Reaction on the surface
Desorption
Diffusion of the reactant
Mass transfer of the product
* Steps 3, 4 and 5 are MOST important

## Slide 6
ERT 208/4 REACTION ENGINEERING
SEM 2 (2009/2010)
Heterogeneous catalyst works in general term;
  (1)Adsorption
  (2)Surface Reaction
  (3)Desorption
HETEROGENEOUS CATALYTIC REACTIONS
Fig 1: Schematic Diagram of Tubular Reactor Packed with Catalytic Pellets

## Slide 7
ERT 208/4 REACTION ENGINEERING
SEM 2 (2009/2010)
Steps in Catalytic Reaction;
HETEROGENEOUS CATALYTIC REACTIONS…cont….
Mass transfer (diffusion) of the reactant(s)(eg. Species A)
Diffusion of the reactant from the pore mouth through the catalyst pores to the immediate vicinity of the internal catalytic surface.
Adsorption of reactant A onto the catalyst surface
Reaction on the surface of the catalyst (eg; A ------B)
Desorption of the products (eg. B) from the surface
Diffusion of the products from the interior of the pellet to the pore mouth at the external surface
Mass transfer of the products from the external pellet surface to the bulk fluid.

## Slide 8: STEP 1:Difussion of the reactant from the bulk to the external transport.

## Slide 9: STEP 2:Internal diffusion

## Slide 10
ERT 208/4 REACTION ENGINEERING
SEM 2 (2009/2010)
Info ;
Overall rate of reaction is equal to the rate of the slowest step in the mechanism.
If diffusion steps (1,2,6 &7) > fast than reaction steps (3,4 &5) – conc in the immediate vicinity of the active sites are indistinguishable from those in the bulk fluid.
- the transport / diffusion steps not effect the overall rate of the reaction.
If reaction steps (3,4&5) > fast than diffusion steps;
- mass transport does effect the reaction rate
HETEROGENEOUS CATALYTIC REACTIONS…cont….

## Slide 11
ERT 208/4 REACTION ENGINEERING
SEM 2 (2009/2010)
In system where diffusion from the bulk gas @ liquid to catalyst surface or to the mouths of catalyst pores effects the rate, changing the flow conditions past the catalyst should change the overall reaction rate.
For porous catalyst, diffusion within the catalyst pores may limit the rate of reaction.
The overall rate will be unaffected by external flow conditions even though diffusion effects the overall reaction rate.
HETEROGENEOUS CATALYTIC REACTIONS…cont….

## Slide 12
STEP 3:Adsorption Isotherms
One unit of species A will be adsorbed on the site S
A atom,molecule,or atomic combination
S
Active site

## Slide 13
ERT 208/4 REACTION ENGINEERING
SEM 2 (2009/2010)
Chemisorptions is usually a necessary part of a catalytic process.
(1) ADSORPTION ISOTHERMS
Where,
S = active sites (alone will donate a vacant site with no atom, molecule/complex adsorp on it)
A.S = mean one unit of “A” will be adsorbed on the site “S”.

## Slide 14
SITE BALANCE:
STEP 3:Adsorption Isotherms
Ct =total concentration of sites
Cv= Vacant site

## Slide 15
ERT 208/4 REACTION ENGINEERING
SEM 2 (2009/2010)
Steps to Describe Isotherm??
Proposed model system
Isotherm model is compared with the experimental data shown on the curve.
If model predicted the curve (agree with exp)-the model reasonably describe what is occurring physically in the real system.
(1)ADSORPTION ISOTHERMS…continue…

## Slide 16
ERT 208/4 REACTION ENGINEERING
SEM 2 (2009/2010)
Example:
Adsorption of Carbon Monoxide
on Metal
1st Step: Proposed model system
– 2 model proposed:
a)As molecule (nondissosiated) - CO
b) As atom (dissociative) - C and O
(1)ADSORPTION ISOTHERMS…continue…

## Slide 17
ERT 208/4 REACTION ENGINEERING
SEM 2 (2009/2010)
MODEL 1: As molecule (nondissosiated) – CO
(MOLECULAR ADSORPTION)
Rate of adsorption:
Rate of desorption:
Net rate of adsorption:
(1)ADSORPTION ISOTHERMS…continue…

## Slide 18
ERT 208/4 REACTION ENGINEERING
SEM 2 (2009/2010)
The rate of attachment (adsorption):
Rate of adsorption for “CO” molecules to the surface directly proportional ;
  to no. of collision that these molecules will make with the surface per second.
  To the product of partial pressure of “CO” & conc of vacant sites.
The rate of detachment (desorption):
Rate of detachment for “CO” molecules to the surface directly proportional ;
  Conc of sites occupied by molecules, CCO.S
(1)ADSORPTION ISOTHERMS…continue…

## Slide 19
ERT 208/4 REACTION ENGINEERING
SEM 2 (2009/2010)
(1)ADSORPTION ISOTHERMS…continue…
At equilibrium;
Because of CO is the only material adsorbed on the catalyst, the site balance gives;

## Slide 20
ERT 208/4 REACTION ENGINEERING
SEM 2 (2009/2010)
(1) ADSORPTION ISOTHERMS…continue…
(1) In (2);
(1)
(2)

## Slide 21
ERT 208/4 REACTION ENGINEERING
SEM 2 (2009/2010)
MODEL 2: As atom (dissosiated) – C and O
(ATOM ADSORPTION)
(1) ADSORPTION ISOTHERMS…continue…
Rate of adsorption:
Rate of desorption:
Net rate of adsorption:

## Slide 22
ERT 208/4 REACTION ENGINEERING
SEM 2 (2009/2010)
(1) ADSORPTION ISOTHERMS…continue…
The rate of attachment (adsorption):
Rate of adsorption for “C and O” atoms to the surface directly proportional ;
  Pressure of CO in the system cz this rate governs the no. of gaseous collision with the surface
  2 adjacent vacant site are required (C.S and O.S)
  2 vacant site occuring adjacent to one another is proportional to square of conc of vacant sites.
  To the product of CO partial pressure & square of vacant
The rate of detachment (desorption):
Rate of detachment for “C and O” atoms to the surface directly proportional ;
  2 occupied sites must be adjacent
  To the product of occupied site conc (C.S and O.S)

## Slide 23
ERT 208/4 REACTION ENGINEERING
SEM 2 (2009/2010)
(1) ADSORPTION ISOTHERMS…continue…
Is adsorption equilibrium constant

## Slide 24
ERT 208/4 REACTION ENGINEERING
SEM 2 (2009/2010)
(1) ADSORPTION ISOTHERMS…continue…
At equilibrium;
Because of C and O is the only material adsorbed on the catalyst, the site balance gives;

## Slide 25
ERT 208/4 REACTION ENGINEERING
SEM 2 (2009/2010)
(1) ADSORPTION ISOTHERMS…continue…
For ;
From,

## Slide 26
ERT 208/4 REACTION ENGINEERING
SEM 2 (2009/2010)
(1) ADSORPTION ISOTHERMS…continue…
Substitute in site balance;
From site balance,
Solving for Cv;

## Slide 27
ERT 208/4 REACTION ENGINEERING
SEM 2 (2009/2010)
(1) ADSORPTION ISOTHERMS…continue…
From;
and
Solving for Co.s ;

## Slide 28
MODEL 1
MOLECULAR
(NONDISSOCIATED ADSORPTION)
CO is adsorbed as molecules CO
MODEL 2
DISSOCIATIVE ADSORPTION
CO is adsorbed as C and O
STEP 3:Adsorption Isotherms
LANGMUIR ISOTHERM

## Slide 29
SINGLE SITE
DUAL SITE
ELEY-RIDEAL
STEP 4:SURFACE REACTION

## Slide 30
STEP 5:DESORPTION
The rate of desorption of C

## Slide 31: The Rate-Limiting Step
When heterogeneous reactions are carried out at steady state. The rates of each of the three reaction steps in series (adsorption, surface reaction and desorption) are equal to one another:
One particular step in the series is usually found to be rate-limiting or rate-controlling.

## Slide 32: ALGORITHM FOR DETERMINING RXN MECHANISM AND RATE LIMITING STEP
Select a mechanism
Assume a rate limiting step:
Choose the surface rxn first
Find the expression for concentration of adsorbed species.
Write a site balance
Derive the rate law
Compare with data

## Slide 33: Synthesizing Rate law, Mechanism and Rate Limiting step
EXAMPLE: Cumene decomposition
CUMENE (C)
BENZENE (B) + PROPYLENE (P)

## Slide 34
EXERCISE 1
ADSORPTION
SURFACE REACTION
DESORPTION
Synthesize the rate law for each mechanism;

## Slide 35: Rate law

## Slide 36
Is the Adsorption of Cumene Rate-Limiting?
Rate of adsorption;
Assume adsorption is rate-limiting, thus;
kA is small and ks and kD are large
The ratio very small ~approximately zero;

## Slide 37
Surface reaction
Desorption
Rearrange;

## Slide 38
Rate of Adsorption;

## Slide 39
To eliminate Cv ;
Cumene rxn rate law if
adsorption are limiting step

## Slide 40
Initially, no products are present; consequently,
PP = PB = 0.
If the cumene decomposition is adsorption rate limited, the initial rate will be linear with the initial partial pressure of cumene

## Slide 41: Is the Surface Reaction Rate-Limiting?
Rate of surface reaction;
Assume surface reaction is rate-limiting, thus;
kS is small and kA and kD are large
The initial rate;
Cumene rxn rate law if
Surface reaction are limiting step

## Slide 42: Is the Surface Reaction Rate-Limiting?

## Slide 43: Is the Desorption of Benzene Rate-Limiting?
Rate of desorption of benzene;
Assume desorption is rate-limiting, thus;
kD is small and kA and kS are large
Cumene rxn rate law if
desorption are limiting step
The initial rate;

## Slide 44: Is the Desorption of Benzene Rate-Limiting?

## Slide 45: SUMMARY OF THE CUMENE DECOMPOSITION
Surface limited reaction mechanism is consistent with experimental data