## Slide 1: Calıbratıon Methods
DR. KADRİYE ÖZLEM HAMALOĞLU
24.12.2018

## Slide 2: Method Valıdatıon
Specificity
Linearity
Accuracy
Precision
Limits of Detection and Quantitation
Range
DR. KADRİYE ÖZLEM HAMALOĞLU
24.12.2018

## Slide 3: Method Valıdatıon - Specıfıcıty
How well an analytical method distinguishes the analyte from everything else in the sample.
Baseline separation
vs.
time
time
DR. KADRİYE ÖZLEM HAMALOĞLU
24.12.2018

## Slide 4: Method Valıdatıon- Lınearıty
How well a calibration curve follows a straight line.
R2 (Square of the correlation coefficient)
DR. KADRİYE ÖZLEM HAMALOĞLU
24.12.2018

## Slide 5: Method Valıdatıon- Accuracy and Precısıon
Precision - reproducibility
Accuracy – nearness to the truth
Compare results from more than one analytical technique
Analyze a blank spiked with known amounts of analyte.
DR. KADRİYE ÖZLEM HAMALOĞLU
24.12.2018

## Slide 6: Method Valıdatıon- LOD and LOQ
Sensitivity
• Limit of detection (LOD) – “the lowest content that can be measured with reasonable statistical certainty.”
• Limit of quantitative measurement (LOQ) – “the lowest concentration of an analyte that can be determined with acceptable precision (repeatability) and accuracy under the stated conditions of the test.”
How low can you go?
DR. KADRİYE ÖZLEM HAMALOĞLU
24.12.2018

## Slide 7: Lımıt of Detectıon (LOD)
• Typically 3 times the signal-to-noise (based on standard deviation of the noise)
Detection limit (lower limit of detection – smallest quantity of analyte that is “statistically” different from the blank.
DR. KADRİYE ÖZLEM HAMALOĞLU
24.12.2018

## Slide 8: Lımıt of Lınear Response (LOL)
• Point of saturation for an instrument detector so that higher amounts of analyte do not produce a linear response in signal.
DR. KADRİYE ÖZLEM HAMALOĞLU
24.12.2018

## Slide 9: Useful Range of an Analytıcal Method
signal
concentration
LOD (Limit of detection)
LOQ (Limit of quantitation)
LOL (Limit of linearity)
Dynamic range
LOD = 3x SD of blank
LOQ = 10x SD of blank
DR. KADRİYE ÖZLEM HAMALOĞLU
24.12.2018

## Slide 10: Method Valıdatıon- sensıtıvıty
signal
concentration
Slope is related to the sensitivity
DR. KADRİYE ÖZLEM HAMALOĞLU
24.12.2018