## Slide 1: KMU 402 FLOW IN CIRCULAR PIPES
Dr. Özge Yüksel Orhan
İlkay Koçer
2019-2020 Spring Semester
Teaching Assistants

## Slide 2
2
THEORY

## Slide 3
Introduction
Transfer
Molecular (Conductive)
Bulk
(Convective)
Newton’s Law
Fourier’s Law
Fick’s Law
3

## Slide 4
Newton’s Law of Viscosity
4
Viscosities of Newtonian Fluids
Gases:
µ T
µ P (> 1000 kPa)
Liquids:
µ T
not effected by pressure
= -µ
Shear stress / shear rate = constant
= viscosity

## Slide 5
Fully Developed Flow Velocity Profile

## Slide 6
Classification of Flow Regimes
Turbulent flow is a flow regime characterized by chaotic property changes. This includes rapid variation of pressure and flow velocity in space and time. In contrast to laminar flow the fluid no longer travels in layers and mixing across the tube is highly efficient.
Laminar flow occurs when a fluid flows in parallel layers, with no disruption between the layers. At low velocities, the fluid tends to flow without lateral mixing, and adjacent layers slide past one another like playing cards.

## Slide 7
Classification of Flow Types
Compressible flow: The fluid density varies significantly in response to a change in pressure.
Incompressible flow: (i) the substance flowing is a liquid or (ii) if it is a gas whose density changes within the system by no more than 10 percent.
Steady flow: The flow properties at every point remain constant with respect to time.
Gravity flow: A flow of liquid drawn under the force of gravity, fall to the ground.

## Slide 8
Derivation of Bernoulli Equation
Continuity Equation:
General Energy Balance:
Overall Mechanical Energy Balance

## Slide 9
Derivation of Bernoulli Equation
Assumptions:
+ g (- +
No mechanical energy is added (Ws = 0)
No friction (
Turbulent flow
Incompressible fluid
Steady state
+ g + + g +

## Slide 10
Friction Losses in Bernoulli Equation
Friction Loss in Straight Pipes
f
laminar
turbulent
f(NRe)
f(NRe , Ɛ/D )
(1) Hagen-Poiseuille Equation:
(2) Friction factor:

## Slide 11
Friction Losses in Bernoulli Equation
Calculation of friction factor
Blasius Equation
(1)
(2)

## Slide 12
Friction Losses in Bernoulli Equation
Sudden Expansion
Sudden Contraction
Bends

## Slide 13
Valves
Gate Valve
Globe Valve
A ball valve has a gate that closes across the flow.
Only fully close or fully open position is required,
Used for on-off control
Small pressure drop across the valve
A globe valve uses a plug (stem) that closes against the flow
Can also be used for the flow regulation
Has a high pressure drop even in fully
open conditions

## Slide 14
Principles of Pressure Loss Measurements
hf = x
s = spesific gravity of mercury
Δh = 12.6x

## Slide 15
Modelling of Efflux Time for a Cylindrical Tank with an Exit Pipe
V1 = V2
z1 = L
z2 = 0
P1 = Patm + hρg
P2 = Patm
Laminar flow
Turbulent flow

## Slide 16
16
EXPERIMENTAL PROCEDURE

## Slide 17: Aim of The Experiment
To study pressure loses due to viscous and localized effects in incompressible fluid flows through pipes,
To make energy balance for a cylindrical tank with an exit pipes of different lengths and diameters,
To calculate energy losses and efflux time,
To compare experimental data with theoretical data.

## Slide 18: Part I – Experimental Setup
The apparatus consists of two separate hydraulic circuits,
one painted dark blue,
one painted light blue,
each one containing a number of pipe system components.
Both circuits are supplied with water from the hydraulic bench.

## Slide 19
Part I – Arrangement of Apparatus
In all cases (except the gate and globe valves) a pair of pressurised piezometer tubes measures the pressure change across each of the components.
In the case of the valves, pressure measurement is made by U-tubes containing mercury.
hydraulic bench

## Slide 20
Part I – Components of Apparatus
Light Blue Circuit
7-8 Sudden Expansion 13.7 mm / 26.4 mm
9-10 Sudden Contraction 26.4 mm/ 13.7 mm
11-12 101.6 mm 90° Radius Bend
13-14 152.4 mm 90° Radius Bend
15-16 50.8 mm 90° Radius Bend
B Globe Valve
Dark Blue Circuit
1-2 Standard Elbow Bend
3-4 Straight Pipe (13.6 mm)
5-6 90° Mitre Bend
A Gate Valve
1
2
6
5
4
3
A
B
14
7
8
9
10
12
13
11
16
15
INLET
OUTLET

## Slide 21
Part I – Experimental Procedure
1. Open fully the water control valve on the hydraulic bench.
2. With globe valve closed, open the gate valve fully to obtain maximum flow through the Dark Blue circuit.

## Slide 22
Part I – Experimental Procedure
3. Record the readings on the piezometer tubes (mm H2O) and the U-tube (mm Hg).

## Slide 23
Part I – Experimental Procedure
4. Record the time to collect 5 L of water in the weighing tank.
5. Repeat the procedure for a total of six different flow rates, obtained by closing gate valve.

## Slide 24
Part I – Experimental Procedure
6. After taking data at six different flow rates, switch off the pump, close the gate valve and open the globe valve.

## Slide 25
Part I – Experimental Procedure
7. Repeat the experimental procedure for the Light Blue circuit.

## Slide 26: Part II – Experimental Setup
The apparatus consists of a cylindrical tank and interchangeable exit pipes of different lengths and diameters.

## Slide 27: Part II – Experimental Setup
1
2
3
4
5
6
L = 8 cm
L = 14.8 cm
L = 30.1 cm
L = 61.4 cm
Dp = 0.17 cm
Dp = 0.22 cm
Dp = 0.355 cm
Dp= 0.28 cm

## Slide 28: Part II – Experimental Procedure
1. Insert the pipe to the
tank.
2. Fill the cylindrical tank
with water.
3. Measure and record the initial time and efflux time for each pipe.

## Slide 29
29
CALCULATIONS

## Slide 30
Part I – Data Sheet

## Slide 31
Part I – Data Sheet

## Slide 32
Part I – Calculations
(1) Calculation of the pressure loss in piezometer tubes
Table 1& Table 6 ( [1-2] and [11-12] )
Table 2 - Table 8
[3-4], [5-6], [7-8], [9-10], [13-14], [15-16]
Test No | 1 2 (mm water) | hL (mm water) | hL (m water) | P1 – P2 (N/m2)
(2) Calculation of the pressure loss in U-tubes
Test No | Valve (mm Hg) | x (mm Hg) | hL (mm water) | hL (mwater) | P1 – P2 (N/m2)
Table 9 & Table 10
x: height difference

## Slide 33
Part I – Calculations
(3) Calculate the friction factor in straight pipes using friction loss and also using Blasius's equation
[This tables will be prepared for [3-4] and [8-9] piezometer tubes]
Table 11& Table 12
Test No | t (s) | m (kg/s) | Q (m3/ s) | V (m/s) | hL (m water) | Re | f (head loss) | f (Blasius)

## Slide 34
Part I – Calculations
(4) Calculation of Loss Coefficient Values for Five Bends
[This tables will be prepared for [1-2], [5-6], [11-12], [13-14] and [15-16] piezometer tubes]
Table 13 - Table 17
Test No | t (s) | m (kg/s) | Q (m3/ s) | V (m/s) | hL (m water) | KB
(5) Calculation of Loss Coefficient Values for Gate and Globe Valves
Draw r/D vs. KB,mean for five bends
Table 18 & Table 19
Test No | t (s) | m (kg/s) | Q (m3/ s) | V (m/s) | x (cm Hg) | hL (m water) | K
Draw flow rate vs. K for the gate valve and the globe valve.
KB, mean
r: bend radii
D: pipe diameter

## Slide 35
Part II – Data Sheet

## Slide 36
Part II – Calculations
(1) Calculation of the initial and final Re Number
Table 20
Test No | D pipe (m) | L pipe (m) | Vinitial (m/s) | Re (initial) | Vfinal (m/s) | Re (final) | f
If Re(final) < 4000
If Re(final) > 4000
(1)
(2)
(3)
(4)
For Re final: Firstly, the flow is assumed as laminar, then from eqn(1), V=Vfinal is found. Then Re(final) is calculated. If the Re(final)<4000, eqn(2) is used to calculate the f value. If the calculated Re(final)>4000, then it is assumed that the flow is turbulent. So from eqn(3) V=Vfinal is
found. After that, Re(final) is calculated. If the Re(final)>4000, eqn(4) is used to calculate the f value.

## Slide 37
Part II – Calculations
(2) Calculation of the kinetic energy values of fluid
Table 21
Test No | D pipe (m) | L pipe (m) | m initial (kg) | Vinitial (m/s) | EK initial (J) | m final (kg) | Vfinal (m/s) | EK final (J) | Delta EK (J)

## Slide 38
Part II – Calculations
Table 22
Test No | D pipe (m) | L pipe (m) | H= H1 (m) | EP1 (J) | m final (kg) | H= H2 (m) | EP2 (J) | Delta EP (J)
(3) Calculation of the potential energy values at h=H1 and h=H2

## Slide 39
Part II – Calculations
(5) Calculation of the efflux time values for each pipe
(4) Calculation of the viscous energy losses in the pipe
Table 23
Test No | D pipe (m) | L pipe (m) | Vfinal (m/s) | f | hf (m)
Test No | D pipe (m) | L pipe (m) | Vinitial (m/s) | Vfinal (m/s) | Vmean (m/s) | Remean | teff (cal.) (s) | teff (exp.) (s)
Laminar
Turbulent
Table 24