## Slide 1: kmu402 Experiment #3: Distillation
Dr. Gökçe Alp
Murat Akdoğan

## Slide 2
Distillation
Material balance
Energy balance
Heat transfer
Mass transfer

## Slide 3
Feed flows down to a stage
Vapor enters the tray and bubbles through the liquid as the liquid flows across
The vapor and liquid leaving the tray are essentially in equilibrium
Vapor continues up to the next stage, where it is again contacted with a downflowing liquid.

## Slide 4: Aim of the experiment:
*Batch
*Continuous
*Feed
*Distillate
*Bottom product
*Reflux
*Relative volatility
*Coning
*Weeping
*Flooding
*Priming
*Column efficiency
*McCabe Thiele method

## Slide 5
Reboiler
Column
Condenser
Feed tank
Top Product Tank

## Slide 6: Overvıew
Experiment will be implemented at 3 parts:
Part I: Batch operation at total reflux
Part II: Batch operation at minimum reflux
Part III: Continuous operation

## Slide 7: Experimental Method
Batch I
Effect of power on several parameters
Power optimization
Batch II
Effect of time
Cont.
Effect of reflux ratio
Min. reflux

## Slide 8: Experimental Method – Part I:
From refractometer
From computer
From column
From U-manometer
via chronometer
0.25
0.50
0.75
1.00
1.25
*Find the optimum power

## Slide 9: Experimental Method – Part II @optimum Power
initial (t=0)
5
10
15
20
25
From refractometer
From computer
*Observe the effect of time

## Slide 10: Experimental Method – Part III Continuous Operation
Optimum power which was found at the first part
50 cm3/min
*Observe the effect of reflux ratio on the products

## Slide 11: Calculations-Part I: Effect of Power on the system
Power (kW) | Boil-up rate (ml/min) | log(Boil-up rate) | 𝝙P (cmH2O) | log𝝙P
0.25 |  |  |  | 
0.50 |  |  |  | 
0.75 |  |  |  | 
1.00 |  |  |  | 
1.25 |  |  |  | 
log𝝙P
log(boil-up rate)
Show weeping & flooding points
Discuss the figure
Boil-up rate = 10 ml / time (min)
Determination of weeping and flooding points

## Slide 12: Calculations-Part I: Effect of Power on the system
Power (kW) | xB | yB | xD | yD | 𝛼AB | Nmin + 1 | Column efficiency
0.25 |  |  |  |  |  |  | 
0.50 |  |  |  |  |  |  | 
0.75 |  |  |  |  |  |  | 
1.00 |  |  |  |  |  |  | 
1.25 |  |  |  |  |  |  | 
Power (kW) | Tav (°C) | 𝜌gas (g/L) | 𝜌liquid (g/L) | Ut (m/min) | Fgt (m/min)(kg/m3)0.5
0.25 |  |  |  |  | 
0.50 |  |  |  |  | 
0.75 |  |  |  |  | 
1.00 |  |  |  |  | 
1.25 |  |  |  |  | 
Fenske Eq. For min. # of stages
Column efficiency = (Nmin/Nactual)*100

## Slide 13: Calculations-Part II: Change of mole fractions with time
t (min) | xB (mole%) | xD (mole%)
0 |  | 
5 |  | 
10 |  | 
15 |  | 
20 |  | 
25 |  | 
30 |  | 
xB
t (min)
t (min)
xD

## Slide 14: Calculations-Part III: Continuous Distillation
RD | xB (mole%) | xD (mole%) | Number of plates | %Efficiency
2 |  |  |  | 
5 |  |  |  | 
10 |  |  |  | 
Effect of Reflux ratio on the Efficiency
«McCabe-Thiele Method»
to calculate the Number of Theoretical Stages
From refractometer

## Slide 15
McCabe Thiele Method
*** An equimolar overflow through the tower.
Total material balance:
Vn+1 + Ln-1 = Vn + Ln
Vn+1yn+1 + Ln-1xn-1 = Vnyn + Lnxn
Component balance on A:
F = D + W,
FxF = DxD +Wxw
Vn , yn
Vn+1 , yn+1
n-1
n
n+1
Ln-1 , xn-1
Ln , xn
feed
F mol/h, xF
Stripping section
Enriching section
distillate
D mol/h, xD
bottoms
W mol/h, xW

## Slide 16
L, D have the same composition, so y1=xD
Equimolar overflow: L1=L2=Ln
V1=V2=Vn
Total material balance : Vn+1 = Ln+D
Component balance: Vn+1yn+1 = Lnxn + DxD
Solving for yn+1, the enriching section operating line is:

## Slide 17
y
x
xD
1
2
n
x1
xn
Slope= Ln/Vn+1
intercept
xD/(R+1)
y1
y1
Reflux ratio: R= Ln/D
Vn+1 = Ln+D,
Ln/Vn+1= R/(R+1)

## Slide 18: Thank you!
Questions?