## Slide 1: COMPOSITE MATERIALS
HACETTEPE UNIVERSITY
DEPARTMENT OF CHEMICAL ENGINEERING
PREPARED BY;
TUĞBA KOÇAK-20519833
SEVİNÇ KARADAĞ-20519756
TOLGA NAİL SEVİNDİK-20574649
ULYA KIBRIS-20772663
KMU 479 MATERIAL SCIENCE AND TECNOLOGY II

## Slide 2: THIS PRESENTATION INCLUDES
11.11.2009
2
What is Composite?
Properties of Composites
Types of Composites
Advantages of Composites
Disadvantages of Composites
Application of Composites
Components of Composites
Producing of Composites

## Slide 3: WHAT IS COMPOSITES?
Composite materials are engineered materials made from two or more constituent materials with significantly different physical or chemical properties which remain separate and distinct on a macroscopic level within the finished structure.
http://en.wikipedia.org/wiki/Composite_material
11.11.2009
3
Notes: http://en.wikipedia.org/wiki/Composite_material

## Slide 4
A cloth of woven carbon fiber filaments, a common element in
composite materials
http://en.wikipedia.org/wiki/Composite_material

## Slide 5: PROPERTIES OF COMPOSITES
Specific strength[1]
Expense[1]
Application[1]
Processability[1]
Orthotropic [2]
Inhomogeneous[3]
Do not dissolve or merge completely into another[4]
[1]http://www.pslc.ws/macrog/mpm/analysis/general.htm
[2]http://en.wikipedia.org/wiki/Composite_material
[3] http://www.sonatest.com/applications/Composite%20Materials.html
[4] http://www.unitedcomposites.net/usapages/whycomposites2.htm
5

## Slide 6: APPLICATION OF COMPOSITES
aircraft industry
space industry
auto and transportation industry
utility industry
chemical industry
http://www.quakewrap.com/frp%20papers/Application-of-Composites-in-Infrastructure-Part-I-and-II-(a-brief-report-on-materials-and-construction).pdf
11.11.2009
6

## Slide 7: some examples of composites
civil infrastructure such as bridges, roads, earthquake retrofitting of buildings etc.
various aircraft, helicopters and rockets
engine parts
marine vessels
sports
printed circuit board
large trucks
shipping containers
tank
ships
http://www.quakewrap.com/frp%20papers/Application-of-Composites-in-
Infrastructure-Part-I-and-II-(a-brief-report-on-materials-and-construction).pdf

## Slide 8
http://www.advancedthermalsupplies.com.au/im/CompositeMaterials/Composites1.gif

## Slide 9: COMPONENTS OF COMPOSITES
Matrix phase: bulk materials such as: Metals, Ceramics, Polymers
Reinforcement: fibers and particulates such as: Glass, Carbon,Kevlar, Silicon Carbide, Boron,Ceramic, MetallicAggregate
Interface: area of mechanical
http://www.ndt-ed.org/EducationResources/CommunityCollage/Materials/Structıre/composite.htm
11.11.2009
9

## Slide 10
Composite properties determined by the matrix:
Transverse mechanical properties
Interlaminar shear strength
Compressive strength
Plasticisation of the matrix
Service temperature
Fire and corrosion resistance
Tool design and fabrication process
http://www.quakewrap.com/frp%20papers/Application-of-Composites-in-Infrastructure-Part-I-and-II-(a-brief-report-on-materials-and-construction).pdf
11.11.2009
10

## Slide 11
Composite properties influenced by fibres:
Rigidity (Modulus of elasticity)
Tensile Longitudinal Strength
Initiation of fracture of fibres
Properties controlled by Interface / bonding:
Fracture energy/Fracture toughness
Interlaminar fracture energy
http://www.quakewrap.com/frp%20papers/Application-of-Composites-in-Infrastructure-Part-I-and-II-(a-brief-report-on-materials-and-construction).pdf
11.11.2009
11

## Slide 12: TYPES OF COMPOSITES
1. Particulate –Reinforced Composite
2. Fiber – Reinforced Composite
3. Structural Composite
3.a. Laminar Composite
3.b. Plate Composite

## Slide 13: 1. Particulate – Reinforced Composite
A composite that consists of tiny particles of one material embedded in another material.
- Particles are most often used to extend the strength or other properties of inexpensive materials by the addition of other materials.
Dr. Uğur SOY, Sakarya Üniversitesi, Kompozit Malzemeler, Ekim 2009

## Slide 14
Particles may have any shape or size, but are generally spherical, ellipsoidal, polyhedral, or irregular in shape.
They may be added to a liquid matrix that later solidifies; grown in place by a reaction such as agehardening.
http://info.lu.farmingdale.edu/depts/met/met205/particlerc.JPG

## Slide 15: 2. Fiber – Reinforced Composite (FRC)
- A FRC consists of three components: (i) fibers as the discontinuous or dispersed phase, (ii) the matrix as the continuous phase, and (iii) the fine interphase region.
Fibers increase the modulus of the matrix material.
The strong covalent bonds along the fiber's length gives them a very high
modulus in this direction.
Dr. Uğur SOY, Sakarya Üniversitesi, Kompozit Malzemeler, Ekim 2009

## Slide 16
- Consideration of orientation and fiber length for a particular composites depends on the level and nature of the applied stress.
- Fibers have a very high modulus along their axis, but have a low modulus perpendicular to their axis.
http://info.lu.farmingdale.edu/depts/met/met205/composites.html

## Slide 17: 3. Structural Composite 3.a. Laminar Composite
- Laminar composites are composed of two-dimensional sheets or panels that have a preferred high strength direction.
Dr. Uğur SOY, Sakarya Üniversitesi, Kompozit Malzemeler, Ekim 2009

## Slide 18: 3. Structural Composite 3.b. Plate Composite
- Composites that composed of plate shape reinforcement agents in the matrix phase.

## Slide 19: ADVANTAGES OF COMPOSITES
Very high specific strength
Great freedom of shape
Less parts, longer life
Material can be tailored
Weight saving
Thermal isolation habits

## Slide 20
Chemical resistance against acids etc.
Weather / water resistance
RAM features (Radar Absorbing Materials)
Electrical habits
Excellent fatigue endurance
Impact habbits
EXCELLENT

## Slide 21
Resistance to corrosion and aggressive media
Reduction of
man-hours needed for maintenance
of structures (painting, repair, replacement of components)
environmental impact
storage costs of semi-finished products

## Slide 22
DISADVANTAGES OF COMPOSITES
High cost (compared to metals)
Expensive raw materials
Manufacturing time
Difficult to repair
Insufficient design data

## Slide 23
It is the fastest growing "materials" market segment
Automotive
Composites are used in a variety of automotive components, from original equipment like driveshafts and truck beds, to after-market equipment like camper shells.
Aerospace
strong enough to take harsh
loading conditions such as
aerospace components (tails,
wings, fuselages, propellers)
http://www.alibaba.com/productshowimg/rahtair-11089275 10758595/Full_Composite_Aircraft_FAJR_3.html
Full Composite Aircraft FAJR-3

## Slide 24
Various composite materials are used in structures such as the Boeing 777 because of their strength, and weight savings. Composites also offer resistance to fatigue, corrosion and impact damage.
http://www.aviation-history.com/theory/composite.htm

## Slide 25
World’s 1st Thermoplastic composite boat hull (courtesy of VT Halmatic Ltd)
Thermoplastic composite wind turbine
http://www.eplcompositesolutions.co.uk/composite/VacuumMouldingCompositeStructures.asp
http://www.eplcompositesolutions.co.uk/composite/VacuumMouldingCompositeStructures.asp
boat and scull hulls
bicycle frames and racing car bodies
fishing rods, storage tanks,
and baseball bats

## Slide 26
chemical industry
engine parts
marine vessels
The need for weight reduction and increased engine rpm in race cars like this one has
motivated serious research into engine valves of carbon fiber-reinforced polymer composites.
Valves molded using the CSU team’s carbon braid-reinforced, high-temperature polyimide resin. Soure: D. Radford, Colorado State University
(http://www.compositesworld.com/articles/composite-engine-valves.aspx)
(http://www.compositesworld.com/articles/composite-engine-valves.aspx)

## Slide 27: Producing OF compositeS
Short fiber- reinforced composites
mixing the fibers with a liquid or plastic matrix
Polymer base composites
Injection molding
Spray-up method
Metal- matrix composites
Casting

## Slide 28: Injection molding method
Figure: www.engineershandbook.com/mfg.method/injectionmolding

## Slide 29: Spray-up method
Figure:www.wacker.com/cms/sprayup.jsp/

## Slide 30: hand lay-up technic
Figure:www.flexidynamic.com/method
The simplest and oldest
Low volume
Labor intensive
For large components

## Slide 31: Pressure bag molding
figure:www.nextcraft.com/media/rc_tips/vacuum_bag_tests
High pressure, usually 30 to 50 psi, gases or vacuum and excess resin are introduced to force the plies together for good bonding during curiying.
By this technique, large polymer matrix component for the skins of military aircraft, tanks, containers, wind turbine blades have been produced.

## Slide 32: Matched die molding
Short fibers or mats are placed in two part die, when die is closed the composite shape is formed.
This method is used for thermoplastics.

## Slide 33: Filament winding
Fibers are wrapped around the mandrel.
The filament is supplied in the polymer matrix resin prior or around the fiber.
Curing is completes the production of the high performance composite.
Figure: www..addax.com/images/technology

## Slide 34
http://www.youtube.com/watch?v=wb1kor4RuPA