## Slide 1
MAD 475 • TUNNELING & SUPPORT DESIGN
Rock Mass Classification Systems in Mining & Tunneling
Engineering Characterization, Empirical Design, and Support Selection Guidelines
INSTITUTION
Hacettepe University, Department of Mining Engineering
Notes: Welcome to MAD 475. Today's 90-minute lecture covers empirical rock mass classification—the critical engineering bridge between geological mapping and structural design in tunneling and underground mining.

## Slide 2
90-MINUTE LECTURE STRUCTURE
Lecture Agenda & Learning Objectives
MODULES 1–3
Foundations & Legacy Systems
MODULES 4–5
Core Quantitative Rating Systems
MODULES 6–7
GSI, Synthesis & Numerical Models
•
Intact Rock vs. Rock Mass: Discontinuities
•
Terzaghi (1946): Rock Load Factor
•
Lauffer (1958): Active Span & Stand-up Time
•
Deere (1967): Core Quality Designation (RQD)
•
Wickham (1972): Rock Structure Rating (RSR)
•
RMR System (Bieniawski 1973/1989): Parameters & Support
•
Mining RMR Extensions: MRMR & MBR Systems
•
Slope Mass Rating (SMR): Slope Adjustments
•
Q-System (Barton 1974/2002): 3 Quotients
•
Support Sizing Charts: vs Engineering Maps
•
Geological Strength Index (GSI): Matrix Chart
•
Constitutive Links: Non-linear Hoek-Brown Model
•
Empirical Correlations:
•
System Comparisons: Strengths & Limitations
•
Design Workflow: Integrated Engineering Pipeline
Notes: Outline the lecture timing: 25 mins on historical foundations and RQD/RSR; 35 mins on RMR and Q-system; 20 mins on GSI and Hoek-Brown linkage; 10 mins on design synthesis and Q&A.

## Slide 3
MODULE 1 • FUNDAMENTALS
Fundamental Mechanics: Intact Rock vs. Rock Mass
+
=
Continuous mineral aggregate bounded between discontinuities. Behavior governed by primary mineralogy, micro-cracks, and grain boundary cementation.
Key Metrics: Uniaxial Compressive Strength (), Young's Modulus (), Tensile Strength ().
Planar structural weaknesses (joints, bedding planes, faults, shears). Impart anisotropic, non-linear shear behavior and high hydraulic permeability.
Key Metrics: Spacing, Persistence, Roughness (), Infilling/Alteration ().
Discontinuous, anisotropic, non-homogeneous assemblage of rock blocks acting as a structural continuum or block system under stress.
Governing Metrics: Mass Modulus (), Cohesion (), Friction Angle (), Hoek-Brown , , .
Intact Rock Material
Discontinuities
Rock Mass System
Notes: Bieniawski's fundamental rule: Rock mass strength is significantly lower than intact rock strength because structural discontinuities dictate macro-scale stability.

## Slide 4
MODULE 1 • GEOLOGICAL INPUTS
Essential Discontinuity Parameters in Engineering
Orientation
Strike and dip relative to tunnel drive axis. Determines kinematic feasibility of block sliding or wedge falls.
Spacing
Perpendicular distance between adjacent discontinuities. Controls individual block size and overall degree of jointing.
Persistence
Discontinuity trace length in exposed rock faces. Defines potential failure plane extent and continuous slip paths.
Roughness
Small-scale asperities and large-scale undulations. Governs inter-block dilation angle and joint shear strength ().
Aperture & Infilling
Perpendicular distance between joint walls and type of gouge (clay, quartz). Controls cohesion loss and wall separation.
Groundwater Inflow
Water pressure () and flow rate. Reduces effective normal stress () and washes out soft joint gouge.
Notes: Discontinuities act as weak links. Point out that orientation relative to excavation direction is often the single most critical parameter determining local wedge stability.

## Slide 5
MODULE 1 • ENGINEERING FUNCTION
Core Objectives of Classification Systems
Bieniawski's Warning
"Rock mass classification is an empirical design aid—it is NOT a replacement for field observations, analytical studies, structural modeling, or sound engineering judgment."
1
2
3
4
Divide Rock Mass into Domain Classes
Categorizes complex, highly variable rock formations into structural regions of similar geotechnical quality.
Provide Standardized Communication
Establishes a quantitative common language between mining engineers, geologists, contractors, and designers.
Derive Quantitative Engineering Inputs
Yields mechanical properties () for analytical calculations and finite element / boundary element numerical simulations.
Recommend Empirical Ground Support
Guides installation of rock bolts, fiber shotcrete, mesh, and steel ribs based on historical case studies.
Notes: Stress to students that empirical systems are preliminary tools. They are invaluable during feasibility studies when data is sparse, but must be cross-checked during final design.

## Slide 6
MODULE 1 • HISTORICAL CONTEXT
Evolution of Major Classification Systems (1879–Present)
1879
Ritter: First empirical approach relating rock conditions to tunnel support needs.
1946
Terzaghi: Rock Load Factor Classification for steel-arch supported rail tunnels (USA).
1958
Lauffer: Stand-up Time vs Active Span relationships (Austria - NATM foundation).
1967
Deere et al.: Rock Quality Designation () quantitative drill-core indexing (USA).
1973/89
Bieniawski: Rock Mass Rating () Geomechanics Classification (South Africa / USA).
1974/02
Barton et al. (NGI): Tunneling Quality Index (-System) for fiber shotcrete design (Norway).
1994/06
Hoek & Brown: Geological Strength Index () for non-linear constitutive numerical models.
Notes: Note the trend: Classification evolved from qualitative descriptive classes (Terzaghi) to quantitative rating indexes (RMR/Q) and finally to constitutive model parameters (GSI).

## Slide 7
MODULE 2 • CLASSICAL EMPIRICAL SYSTEMS
Terzaghi's Rock Load Classification (1946)
First comprehensive classification in English integrating geology into tunnel support design. Designed specifically for sizing heavy steel sets in blasted rail tunnels.
Mechanics of Load Transfer
When a tunnel is excavated, the surrounding rock mass tends to yield into the opening. A parabola of loosened rock of height detaches and rests its full dead weight upon the support structure.
Arching action transfers the weight of the remaining overburden to the sides of the tunnel opening.
= Equivalent roof support pressure ()
= Height of loosened rock zone above tunnel crown ()
= Unit weight of the rock mass ()
= Tunnel width (), = Tunnel height ()
Notes: Explain rock load factor. Terzaghi categorized rock into 9 classes based on jointing, swelling, and squeezing potential to estimate .
Explain 𝐻_𝑝 rock load factor. Terzaghi categorized rock into 9 classes based on jointing, swelling, and squeezing potential to estimate 𝐻_𝑝.

## Slide 8
Class | Rock Condition Description | Rock Load Factor (feet) | Support Sizing Remarks
I | Hard and intact (no joints/fractures) |  | No support required; spot bolts for spalling
II | Hard stratified or schistose |  | Light crown support against spalling
III | Massive, moderately jointed |  | Light support; vertical walls self-supporting
IV | Moderately blocky and seamy |  | No side pressure; support load on crown
V | Very blocky and seamy (closely jointed) |  | Little/no side pressure; heavy roof support
VI | Completely crushed but chemically intact |  | Considerable side pressure; circular sets
VII | Squeezing rock at moderate depth () |  | Heavy side pressure; yieldable circular arches
VIII | Squeezing rock at great depth () |  | Very heavy yieldable circular arches + invert
IX | Swelling rock (moisture-active clays) |  | Heavy yielding circular ribs with invert struts
Class | Rock Condition Description |  | Support Sizing Remarks
I | Hard and intact (no joints/fractures) |  | No support required; spot bolts for spalling
II | Hard stratified or schistose |  | Light crown support against spalling
III | Massive, moderately jointed |  | Light support; vertical walls self-supporting
IV | Moderately blocky and seamy |  | No side pressure; support load on crown
V | Very blocky and seamy (closely jointed) |  | Little/no side pressure; heavy roof support
VI | Completely crushed but chemically intact |  | Considerable side pressure; circular sets
VII |  |  | Heavy side pressure; yieldable circular arches
VIII |  |  | Very heavy yieldable circular arches + invert
IX | Swelling rock (moisture-active clays) |  | Heavy yielding circular ribs with invert struts
MODULE 2 • TERZAGHI SYSTEM
Terzaghi Rock Classes & Rock Load Factors ()
Notes: Note rules of thumb: Below groundwater table, reduce loads by 50% for dry tunnels above table (Rose 1982). For TBM excavations, reduce by 20–25% due to reduced blast disturbance.
Note rules of thumb: Below groundwater table, reduce loads by 50% for dry tunnels above table (Rose 1982). For TBM excavations, reduce 𝐻_𝑝 by 20–25% due to reduced blast disturbance.

## Slide 9
MODULE 2 • SYSTEM EVALUATION
Limitations of Terzaghi's Rock Load Method
1. Overestimates Support for Large Spans
Accurate for small tunnels (), but yields overly conservative, excessive rock load estimates for large-span openings () (Singh & Goel 1999).
2. Limited to Steel Arch Supports
Developed specifically for passive steel ribs. Does not account for modern active rock reinforcement like fully-grouted rock bolts, cable bolts, or sprayed shotcrete shell linings (Cording & Deere 1972).
3. Subjective Qualitative Rock Inputs
Relies on descriptive terms ("blocky and seamy", "crushed") without objective numerical measurement parameters like RQD, joint spacing, or joint shear strength (Cecil 1970).
4. Wide Squeezing/Swelling Ranges
Load ranges for classes VII–IX are too broad to allow precise engineering design without extensive secondary field stress measurements.
Notes: Summarize: While Terzaghi was a massive historical leap forward, its conservatism and focus on steel ribs necessitated modern multi-parameter quantitative systems.

## Slide 10
MODULE 2 • CLASSICAL EMPIRICAL SYSTEMS
Lauffer's Stand-Up Time Concept (1958)
Foundation of NATM: Lauffer showed that as active span increases, stand-up time decreases exponentially. This principle forms the base of the New Austrian Tunneling Method (Pacher et al. 1974).
Lauffer's Rock Mass Classes
Classified rock mass quality into 7 categories:
Definition: Active Unsupported Span
The unsupported tunnel section width, or the distance from the excavated tunnel face to the nearest installed permanent support (if greater than tunnel span).
Definition: Stand-Up Time
The elapsed time span during which an excavated active tunnel span can remain open without any support or reinforcement before collapse begins.
Class A: Very Good (Indefinite stand-up time)
Class B: Good
Class C: Fair
Class D: Poor
Class E: Very Poor
Class F: Extremely Poor
Class G: Completely Crushed / Squeezing
Notes: Emphasize: In NATM, support must be installed within the stand-up time window to prevent ring closure collapse while allowing controlled stress relief.

## Slide 11
MODULE 2 • RECONSTRUCTED DIAGRAM
Active Span vs. Stand-Up Time Relationships
Key Design Insight
In Class E rock (Very Poor), a span will collapse in less than 1 hour if left unsupported.
Class A (Very Good)
A span can stand unsupported for over 20 years without structural decay.
RMR Linkage
Bieniawski later correlated these curves directly with numeric RMR rating bands (, ).
Notes: Walk students through reading the chart. Highlight how active span size dramatically compresses available stand-up time in poorer rock classes.

## Slide 12
MODULE 2 • PARADIGM SHIFT
Transition to Quantitative Multi-Parameter Systems
Why Single Indicators Fail
Multi-Parameter Quantitative Solution
•
Qualitative Ambiguity: Terms like "moderately jointed" mean different things to different engineers.
•
Single Parameter Blindness: Intact rock strength alone does not govern stability when joints control failure.
•
Ignoring Ground Water: Pore water pressure drastically reduces joint friction without altering core appearance.
•
In-situ Stress Ignored: Deep high-stress rock bursts cannot be predicted by shallow load factors.
•
Objective Indexing: Uses measured core lengths, joint counts, laboratory strength, and water inflows.
•
Mathematical Combination: Combines parameters via addition (RMR) or multiplicative ratios (Q).
•
Direct Support Maps: Output maps directly to concrete shotcrete thickness, bolt lengths, and spacing.
•
Numerical Modeling Input: Directly yields equivalent deformation modulus () and Mohr-Coulomb parameters.
Notes: We now examine core quantitative parameters, starting with Deere's Rock Quality Designation (RQD).

## Slide 13
MODULE 3 • CORE QUANTITATIVE PARAMETERS
Rock Quality Designation (RQD) (Deere 1967)
RQD quantifies degree of jointing/fracturing from drill core. Defined as percentage of intact core pieces () in total core run using standard diameter core ().
RQD Classification Scale
Standard Logging Rules
•
Only hard, intact core pieces are summed.
•
Mechanical breaks caused by drilling must be fitted together and counted as unbroken intact pieces.
•
Weathered, soft, or highly altered core pieces are excluded even if .
RQD Value (%) | Rock Mass Quality Class
 | Very Poor
 | Poor
 | Fair
 | Good
 | Excellent
RQD Value (%) | Rock Mass Quality Class
 | Very Poor
 | Poor
 | Fair
 | Good
 | Excellent
Notes: Emphasize: RQD is a standard input parameter in both Bieniawski's RMR and Barton's Q-system.

## Slide 14
MODULE 3 • RQD MECHANICS
RQD Measurement Procedure & Worked Example
Core Run Total Length = 200 cm
Calculation Steps
Sum of sound pieces :
38 + 30 + 30 + 40 + 30 = 168 cm
Divide by total run length ():
Result Classification: "GOOD" Rock Mass Quality ().
38 cm
✓ Counted (> 10 cm)
8 cm
✗ Discarded (< 10 cm)
30 cm
✓ Counted (> 10 cm)
4
cm
✗ Discarded (< 10 cm)
30 cm
✓ Counted (> 10 cm)
40 cm
✓ Counted (> 10 cm)
5 cm
✗ Discarded (< 10 cm)
30 cm
✓ Counted (> 10 cm)
Notes: Point out the traps: Drilling mechanical breaks must be fitted together and logged as unbroken core. Soft clayey core pieces are excluded due to lack of sound intact matrix.
Point out the traps: Drilling mechanical breaks must be fitted together and logged as unbroken core. Soft clayey core pieces >10" cm" are excluded due to lack of sound intact matrix.

## Slide 15
MODULE 3 • OUTCROP ESTIMATION
RQD Estimation from Volumetric Joint Count ()
Note: If , . If , . is extremely useful during preliminary geological field mapping before drilling begins.
When drill core is unavailable (e.g. surface mapping or adit mapping), Palmström (1982) derived a direct correlation between RQD and Volumetric Joint Count () for clay-free rock masses.
Major Advantage of
Direct borehole logging suffers heavily from directional orientation bias (boreholes parallel to a major joint set miss joints and overestimate RQD).
Using 3D volumetric joint count () eliminates orientation bias and yields a representative spatial rock mass index.
Volumetric Joint Count Formula ()
is the sum of the number of joints per meter for all joint sets:
Where = average joint spacing (m) for set , = number of random joints per .

## Slide 16
MODULE 3 • PARAMETER EVALUATION
Critical Limitations of the RQD Index
RQD is a valuable index parameter, but NEVER use RQD as a standalone rock engineering design index.
1. Directional Borehole Sensitivity
A borehole drilled parallel to a dominant joint set encounters few joints (), whereas a perpendicular borehole in identical rock yields .
2. Insensitive to Joint Surface Condition
Treats unweathered, rough, tightly interlocked joints identically to smooth, slickensided joints filled with soft swelling clay.
3. Step-Function Arbitrary Threshold
A core piece of scores , while a piece of scores . This creates artificial step-function distortions in uniform joint spacing.
4. Insensitive at High Fracture Frequencies
When fracture frequency exceeds , RQD drops to and loses all capacity to differentiate between moderately broken and completely crushed rock (Palmström & Broch 2006).

## Slide 17
MODULE 3 • WICKHAM SYSTEM (1972)
Rock Structure Rating (RSR) Overview
RSR support charts. RSR provided charts for 10 ft, 20 ft, and 24 ft tunnels recommending shotcrete thickness, bolt spacing, and steel rib spacing.
Developed by Wickham et al. (1972) from case histories of small steel-supported tunnels. First complete quantitative rating model to make reference to shotcrete support.
Historical Significance
RSR introduced the concept of combining geological factors (), structural geometry (), and hydrogeology () into a single normalized numerical index ().
Directly inspired Bieniawski's Rock Mass Rating (RMR) system. Note: RSR tables use Imperial units.
Rock origin (igneous, metamorphic, sedimentary), rock hardness, and structural folding/faulting.
Joint spacing, joint orientation relative to tunnel axis, and drive direction (with/against dip).
Combined sum of A+B, joint surface condition (good/fair/poor), and water inflow rate (gpm/1000 ft).
Parameter A: Geology
Max 30 pts
Parameter B: Geometry
Max 45 pts
Parameter C: Water & Joints
Max 25 pts

## Slide 18
MODULE 3 • RSR APPLICATION
RSR Ground Support Prediction Curves ( Tunnel)
Economic Sizing Trade-Off
RSR allowed engineers to compare costs between alternative support systems: steel arches vs rock bolts + shotcrete for a given tunnel diameter.
High RSR ()
Massive rock requires no rib support or light spot bolting.
Low RSR ()
Heavily jointed rock requires heavy steel ribs spaced apart or shotcrete lining.
Notes: Transition to Module 4. We now delve into Bieniawski's Rock Mass Rating (RMR) system—the most globally utilized civil/mining classification system.

## Slide 19
MODULE 4 • BIENIAWSKI SYSTEM (1973/1989)
Bieniawski's Rock Mass Rating (RMR) System
RMR basic sums parameters 1–5 (Max 100). Parameter 6 is an explicit penalty adjustment based on whether joint dip/strike orientation is favorable or unfavorable.
The Geomechanics Classification (RMR) evaluates 6 basic parameters to derive a total score ranging from 0 to 100. Higher numerical ratings indicate better rock mass quality.
Structural Regions
In field application, the site is first divided into distinct structural regions separated by major faults or lithological boundaries.
Each structural region is classified independently using the RMR rating breakdown.
1. UCS (): Max 15 pts
2. RQD (%): Max 20 pts
3. Joint Spacing: Max 20 pts
4. Joint Condition: Max 30 pts
5. Groundwater: Max 15 pts
6. Orientation Adjust: 0 to -60 pts

## Slide 20
Qualitative Class | (MPa) | (MPa) | Rating
Exceptionally High |  |  | 15
Very High |  |  | 12
High |  |  | 7
Medium |  |  | 4
Low |  | Use | 2
Very Low |  | Use | 1
Extremely Low |  | Use | 0
Qualitative Class |  |  | Rating
Exceptionally High |  |  | 15
Very High |  |  | 12
High |  |  | 7
Medium |  |  | 4
Low |  |  | 2
Very Low |  |  | 1
Extremely Low |  |  | 0
RQD Rating Band (%) | Qualitative Designation | Rating
 | Excellent | 20
 | Good | 17
 | Fair | 13
 | Poor | 8
 | Very Poor | 3
RQD Rating Band (%) | Qualitative Designation | Rating
 | Excellent | 20
 | Good | 17
 | Fair | 13
 | Poor | 8
 | Very Poor | 3
MODULE 4 • RATING PARAMETERS
RMR Parameters 1 & 2: Intact Strength & RQD
Intact matrix properties account for up to 35 points combined out of 100 in basic RMR.
Note: For low strength ranges (), point load testing is invalid; use UCS uniaxial lab testing.
1. Intact Strength ( / )
Max 15 pts
2. Core Quality Designation ()
Max 20 pts

## Slide 21
Spacing Range | Description | Rating
 | Very Wide | 20
 | Wide | 15
 | Moderate | 10
 | Close | 8
 | Very Close | 5
Spacing Range | Description | Rating
 | Very Wide | 20
 | Wide | 15
 | Moderate | 10
 | Close | 8
 | Very Close | 5
Sub-Parameter | Best Condition (6 pts) | Worst Condition (0 pt)
Persistence | length | length
Aperture | None (Tight) | open
Roughness | Very Rough | Slickensided
Infilling | Hard / None | Soft gouge
Weathering | Unweathered | Decomposed
Sub-Parameter | Best Condition (6 pts) | Worst Condition (0 pt)
Persistence |  | 
Aperture | None (Tight) | 
Roughness | Very Rough | Slickensided
Infilling |  | 
Weathering | Unweathered | Decomposed
MODULE 4 • RATING PARAMETERS
RMR Parameters 3 & 4: Joint Spacing & Condition
Parameter 4 is the heaviest individual weighted component (30 points). Roughness and infilling gouge dictate whether joints develop friction or slip freely.
Evaluated via 5 sub-parameter ratings (6 pts max each):
3. Discontinuity Spacing
Max 20 pts
4. Condition of Discontinuities
Max 30 pts

## Slide 22
Inflow / 10m | Ratio | Condition | Rating
None |  | Completely Dry | 15
 |  | Damp | 10
 |  | Wet | 7
 |  | Dripping | 4
 |  | Flowing | 0
Inflow / 10m |  | Condition | Rating
None |  | Completely Dry | 15
 |  | Damp | 10
 |  | Wet | 7
 |  | Dripping | 4
 |  | Flowing | 0
Assessment | Tunnels | Foundations | Slopes
Very Favorable |  |  | 
Favorable |  |  | 
Fair |  |  | 
Unfavorable |  |  | 
Very Unfavorable |  |  | 
Assessment | Tunnels | Foundations | Slopes
Very Favorable |  |  | 
Favorable |  |  | 
Fair |  |  | 
Unfavorable |  |  | 
Very Unfavorable |  |  | 
MODULE 4 • RATING ADJUSTMENTS
RMR Parameter 5 (Water) & Orientation Adjustments
Stress tunneling strike/dip rule: Driving perpendicular to joint strike and driving WITH dip () yields the safest arch geometry.
Drive with dip () = Very Favorable. Drive against dip () = Unfavorable.
5. Groundwater Condition
Max 15 pts
6. Discontinuity Orientation Penalty
0 to -60 pts

## Slide 23
RMR Score | Class No. | Description | Average Stand-up Time | Mass Cohesion () | Friction Angle ()
100 – 81 | Class I | Very Good Rock | 20 years for span | () | 
80 – 61 | Class II | Good Rock | 1 year for span |  | 
60 – 41 | Class III | Fair Rock | 1 week for span |  | 
40 – 21 | Class IV | Poor Rock | 10 hours for span |  | 
$< 20$ | Class V | Very Poor Rock | 30 minutes for span | () | 
RMR Score | Class No. | Description | Average Stand-up Time |  | 
100 – 81 | Class I | Very Good Rock |  |  | 
80 – 61 | Class II | Good Rock |  |  | 
60 – 41 | Class III | Fair Rock |  |  | 
40 – 21 | Class IV | Poor Rock |  |  | 
$< 20$ | Class V | Very Poor Rock |  |  | 
MODULE 4 • FINAL CLASS DETERMINATION
RMR Rock Mass Classes & Mechanical Properties
Mohr-Coulomb mapping: RMR converts field observations into quantitative mechanics ( and ) required by geotechnical engineers.
Direct Output: Mohr-Coulomb Provides equivalent rock mass cohesion () and friction angle () directly for limit-equilibrium stability calculations.
Stand-Up Guidance Determines allowable unsupported excavation span and time delay before primary support must be installed.

## Slide 24
MODULE 4 • GEOMECHANICAL INPUT
Estimating Rock Mass Modulus () from RMR
Without , finite element simulations will severely underestimate tunnel wall deformations and ground surface settlement basins.
Numerical Simulation Role
In finite element (FEA) or finite difference (FLAC) codes, intact rock modulus () overestimates mass stiffness by due to joint compliance.
Empirical equations scale down to equivalent mass deformation modulus () to accurately predict surface settlement and tunnel convergence.
Bieniawski (1978) (for $RMR > 50$)
Serafim & Pereira (1983) (for or )
Galera et al. (2005) (Continuous Range)

## Slide 25
Class | Excavation Advance | Rock Bolts ( grouted) | Shotcrete | Steel Sets
I • Very Good RMR: 81-100 | Full face; advance | Generally no support except spot bolting | None | None
II • Good RMR: 61-80 | Full face; advance; complete support from face | Locally bolts in crown long, spaced with mesh | in crown where required | None
III • Fair RMR: 41-60 | Top heading & bench; advance in top heading | Systematic bolts long, spaced in crown & walls with mesh | crown, sides | None
IV • Poor RMR: 21-40 | Top heading & bench; advance; support concurrently with excavation | Systematic bolts long, spaced in crown & walls with mesh | crown, sides | Light/medium ribs spaced where required
V • Very Poor RMR: | Multiple drifts; advance; shotcrete immediately after blasting | Systematic bolts long, spaced ; bolt invert | crown, sides, face | Medium/heavy ribs spaced with forepoling & closed invert
Class | Excavation Advance |  | Shotcrete | Steel Sets
I • Very Good RMR: 81-100 |  | Generally no support except spot bolting | None | None
II • Good RMR: 61-80 |  |  |  | None
III • Fair RMR: 41-60 |  |  |  | None
IV • Poor RMR: 21-40 |  |  |  | 
MODULE 4 • BIENIAWSKI SUPPORT TABLE
RMR Support Guidelines ( Span Horseshoe Tunnel)
For drill-and-blast horseshoe tunnels depth, modern engineering practice frequently replaces wire mesh + shotcrete with steel fiber reinforced shotcrete (SFRS).

## Slide 26
MODULE 4 • MINING APPLICATIONS
Modifications to RMR for Underground Mining
Contrast in civil vs mining tunneling: Civil tunnels maintain static equilibrium. Mining excavations experience dynamic stress changes as the face moves.
Tailored specifically for block caving and hard rock mining operations where stresses dynamically redistribute (Laubscher 1990).
Developed for block cave development drifts, extraction horizons, and major drawpoint intersections (Cummings et al. 1982).
LAUBSCHER System
Modified RMR ()
Adjustment Factors Applied to Basic RMR:
KENDORSKI System
Modified Basic RMR ()
Key Modifications:
•
In-situ and induced mining stresses
•
Stress changes due to face advancement
•
Blasting damage adjustments
•
Environmental weathering exposure over time
•
Differs parameter weightings for fault gouge
•
Distance adjustments relative to active face
•
Provides specific support designs for isolated drifts vs long-term intersections

## Slide 27
SMR Score | Class | Stability | Failure Mode
81 – 100 | I • Very Good | Completely Stable | None
61 – 80 | II • Good | Stable | Some blocks
41 – 60 | III • Fair | Partially Stable | Some wedges
21 – 40 | IV • Poor | Unstable | Planar / Large wedges
0 – 20 | V • Very Poor | Completely Unstable | Circular / Mass flow
MODULE 4 • SLOPE MASS RATING
Slope Mass Rating () (Romana 1985)
SMR evaluates planar sliding and toppling mechanisms. Notice penalizes joint sets that daylight into the slope face ().
Extends Bieniawski's basic RMR for rock slope engineering by incorporating specific structural adjustment factors for joint orientation and excavation method.
SMR Stability Classes
: Parallelism between joint strike and slope face strike ().
: Joint dip angle in planar mode (). for toppling.
: Relationship between slope dip and joint dip ().
: Excavation method (Natural slope , Presplit , Smooth blast , Blasting , Deficient blast ).

## Slide 28
MODULE 5 • BARTON SYSTEM (1974/2002)
Norwegian Tunneling Quality Index (-System)
Q-value is calculated from 6 parameters grouped into 3 distinct mathematical ratios.
Developed at NGI by Barton, Lien, and Lunde (1974) based on 212 Scandinavian hard rock tunnel case histories.
Defines an open logarithmic index ranging from 0.001 (Exceptionally Poor) to 1000 (Exceptionally Good).
6 Basic Input Parameters
Additive vs Multiplicative Logic
Unlike RMR (which sums parameters linearly), the Q-System multiplies three structural quotients representing independent physical parameters.
1. : Rock Quality Designation percentage
2. : Joint Set Number (number of sets)
3. : Joint Roughness Number
4. : Joint Alteration / Filling Number
5. : Joint Water Reduction Factor
6. : Stress Reduction Factor

## Slide 29
MODULE 5 • MATHEMATICAL STRUCTURE
The Q-System Equation: Three Structural Quotients
Physical insight: Quotient 1 = block geometry; Quotient 2 = inter-block friction; Quotient 3 = active stress environment.
QUOTIENT 1
Relative Block Size
Measures visual particle/block size. High RQD combined with few joint sets () yields large, massive intact blocks.
QUOTIENT 2
Inter-block Shear Strength
Represents joint surface friction (). Rough, un-altered joints in direct contact score high.
QUOTIENT 3
Active Stress State
Empirical stress factor. High pore water pressure or heavy squeezing/rock burst conditions severely lower this quotient.

## Slide 30
Description / Joint Frequency | Rating
Massive, no or few joints | 0.5 – 1.0
One joint set | 2.0
One joint set plus random joints | 3.0
Two joint sets | 4.0
Two joint sets plus random joints | 6.0
Three joint sets | 9.0
Three joint sets plus random joints | 12.0
Four or more joint sets, heavily jointed | 15.0
Crushed rock, earthlike aggregate | 20.0
Description / Joint Frequency | 
Massive, no or few joints | 0.5 – 1.0
One joint set | 2.0
One joint set plus random joints | 3.0
Two joint sets | 4.0
Two joint sets plus random joints | 6.0
Three joint sets | 9.0
Three joint sets plus random joints | 12.0
Four or more joint sets, heavily jointed | 15.0
Crushed rock, earthlike aggregate | 20.0
MODULE 5 • Q PARAMETER DETAILS
Quotient 1: Joint Set Number () Sizing
Why intersections use : At tunnel intersections, geometry creates extra degrees of freedom for block detachment.
Joint Set Rating Table ()
Special Field Rules for
•
Tunnel Intersections: Multiply by ().
•
Portal Zones: Multiply by () to account for surface stress relaxation.
•
Nominal : If measured , use a fixed nominal value of in formula.

## Slide 31
Joint Wall Contact Condition | 
Discontinuous joints | 4.0
Rough or irregular, undulating | 3.0
Smooth, undulating | 2.0
Slickensided, undulating | 1.5
Rough or irregular, planar | 1.5
Smooth, planar | 1.0
Slickensided, planar | 0.5
Continuous thick clay gouge (no contact) | 1.0
Joint Wall Contact Condition | 
Discontinuous joints | 4.0
Rough or irregular, undulating | 3.0
Smooth, undulating | 2.0
Slickensided, undulating | 1.5
Rough or irregular, planar | 1.5
Smooth, planar | 1.0
Slickensided, planar | 0.5
Continuous thick clay gouge (no contact) | 1.0
Gouge / Infilling Description |  | 
Tightly healed, quartz/epidote | — | 0.75
Unaltered walls, surface staining |  | 1.0
Slightly altered, sandy particles |  | 2.0
Silty / sandy clay coatings |  | 3.0
Softening mica/talc/chlorite coatings |  | 4.0
Continuous swelling clay () |  | 8 – 12
Thick continuous swelling clay band |  | 13 – 20
Gouge / Infilling Description |  | 
Tightly healed, quartz/epidote | — | 0.75
Unaltered walls, surface staining |  | 1.0
Slightly altered, sandy particles |  | 2.0
Silty / sandy clay coatings |  | 3.0
Softening mica/talc/chlorite coatings |  | 4.0
 |  | 8 – 12
Thick continuous swelling clay band |  | 13 – 20
MODULE 5 • Q PARAMETER DETAILS
Quotient 2: Joint Roughness () & Alteration ()
Note rule for : Evaluate and for the joint set or weakness plane that is LEAST favorable for structural stability in orientation.
Joint Roughness ()
Joint Alteration ()

## Slide 32
Water Inflow / Pressure | 
Dry excavation or minor inflow () | 1.0
Medium inflow, occasional outwash of filling | 0.66
Large inflow / high pressure in open joints | 0.50
Large inflow, severe outwash of fillings | 0.33
Exceptionally high inflow decaying with time | 0.2 – 0.1
Exceptionally high inflow continuing without decay | 0.1 – 0.05
Water Inflow / Pressure | 
 | 1.0
Medium inflow, occasional outwash of filling | 0.66
Large inflow / high pressure in open joints | 0.50
Large inflow, severe outwash of fillings | 0.33
Exceptionally high inflow decaying with time | 0.2 – 0.1
Exceptionally high inflow continuing without decay | 0.1 – 0.05
Stress Condition Domain |  | 
Multiple shear zones in weak rock | — | 10.0
Competent rock, medium favorable stress |  | 1.0
High stress, tight structure (favorable) |  | 0.5 – 2.0
Moderate slabbing / spalling after |  | 5 – 50
Heavy rock burst / strain burst in massive rock |  | 200 – 400
Heavy squeezing rock pressure | — | 10 – 20
Stress Condition Domain |  | 
Multiple shear zones in weak rock | — | 10.0
Competent rock, medium favorable stress |  | 1.0
High stress, tight structure (favorable) |  | 0.5 – 2.0
 |  | 5 – 50
Heavy rock burst / strain burst in massive rock |  | 200 – 400
Heavy squeezing rock pressure | — | 10 – 20
MODULE 5 • Q PARAMETER DETAILS
Quotient 3: Joint Water () & Stress Reduction ()
Stress reduction factor () reflects 3 physical cases: 1) loosening load in fault zones; 2) rock bursting in hard high-stress rock; 3) squeezing in soft plastic rock.
Water Reduction Factor ()
Stress Reduction Factor ()

## Slide 33
Excavation Category | ESR
A. Temporary mine openings | 3.0 – 5.0
B. Permanent mine openings, hydro water tunnels, pilot drifts | 1.6
C. Storage caverns, minor road/rail tunnels, access drifts | 1.3
D. Power stations, major railway/highway tunnels, portals | 1.0
E. Nuclear power stations, underground sports arenas, factories | 0.8
MODULE 5 • SUPPORT DIMENSIONING
Equivalent Dimension () & Support Ratio ()
ESR reflects allowable risk. A temporary mine opening () accepts minor spalling, permitting lighter support than a nuclear facility ().
To design tunnel support using the Q-system, the actual tunnel dimensions are normalized into an Equivalent Dimension () using the Excavation Support Ratio ().
Use roof span width for designing roof support. Use wall height for designing sidewall support.
ESR Category Values (Barton et al. 1974)

## Slide 34
MODULE 5 • RECONSTRUCTED ENGINEERING CHART
Barton Q Support Chart ( vs -Index)
Bolt Length Formula ()
Where = tunnel excavation span width (m).
Max Unsupported Span ()
Notes: Demonstrate using chart: Plot $Q$ on horizontal axis and $D_e$ on vertical axis. Their intersection selects one of 38 support categories (Grimstad & Barton 1993).

## Slide 36
MODULE 5 • MODERN Q MODIFICATIONS
UCS Normalized Index () & Roof Support Pressure
If is low (smooth planar joints), increases rapidly because joint wall friction is inadequate to prevent block dropouts.
To adjust for intact rock strength () variations in unusually soft or hard rocks, Barton (2002) introduced the normalized index:
Steel Fiber Shotcrete (SFRS) Era
Since the 1990s, Grimstad & Barton updated the support chart to mandate Steel Fiber Reinforced Shotcrete (SFRS) instead of wire mesh.
SFRS forms an active ductile arches shell bonded directly to the irregular rock perimeter, preventing wedge fallout.
Permanent Roof Support Pressure ()
Estimated directly from and joint roughness ():

## Slide 37
MODULE 5 • EMPIRICAL CORRELATIONS
Rock Mass Modulus () & Squeezing Thresholds
Squeezing Mechanics
When depth , in-situ overburden stress exceeds the ultimate rock mass compressive strength ().
The rock slowly advances plastically into the tunnel without volume increase. Requires yielding support arches and immediate invert closure.
Barton (1995) Modulus (for )
Barton (2002) Strength-Normalized Modulus
Squeezing Condition Threshold (Singh et al. 1992)
Tunneling under depth (meters) experiences plastic squeezing when:
Notes: We now examine Hoek's Geological Strength Index (GSI)—developed specifically to feed non-linear numerical constitutive models.

## Slide 38
MODULE 6 • HOEK & BROWN SYSTEM (1994)
Geological Strength Index () Genesis
GSI is NOT a support table lookup like RMR or Q. GSI is a constitutive input generator for numerical simulation engines.
Introduced by Evert Hoek (1994) to overcome severe limitations of RMR when applied to heavily jointed, weak, or tectonically sheared rock masses.
Relies on visual assessment of two fundamental geological observations: Rock Mass Structure (interlocking) and Joint Surface Quality.
Geological Observation First
Hoek designed GSI to keep engineers focused on visual geological mapping in the adit face rather than getting lost in laboratory arithmetic formulas.
GSI Scale Range: 10 (Crushed/Sheared) to 100 (Intact Massive).
Primary Engineering Purpose
Provides a direct qualitative/quantitative index to scale intact laboratory Hoek-Brown failure parameters () down to field rock mass strength parameters ().

## Slide 40
MODULE 6 • GSI MATRIX LOGIC
GSI Matrix Architecture: Two Fundamental Axes
Diagonal contouring: The intersection box selected by the geologist yields an average diagonal contour value (e.g., GSI = 45–55).
+
VERTICAL AXIS
Rock Mass Structure
Measures degree of block interlocking and joint set density:
HORIZONTAL AXIS
Discontinuity Surface Quality
Measures weathering, roughness, and infilling coatings:
•
Intact / Massive: Few widely spaced joints
•
Blocky: Well interlocked cubical blocks (3 joint sets)
•
Very Blocky: Multi-faceted angular blocks (4+ sets)
•
Blocky / Folded: Heavily folded/faulted angular blocks
•
Crushed: Poorly interlocked, heavily broken mixture
•
Very Good: Very rough, fresh, unweathered surfaces
•
Good: Rough, slightly weathered, stained surfaces
•
Fair: Smooth, moderately weathered/altered
•
Poor: Slickensided, highly weathered with compact coatings
•
Very Poor: Slickensided with soft clay coatings

## Slide 41
Structure / Surface | VERY GOOD Rough, Unweathered | GOOD Rough, Stained | FAIR Smooth, Weathered | POOR Slickensided | VERY POOR Soft Clay Coatings
BLOCKY (3 joint sets) | GSI 80 | GSI 70 | GSI 60 | GSI 50 | GSI 40
VERY BLOCKY (4+ sets) | GSI 70 | GSI 60 | GSI 50 | GSI 40 | GSI 30
BLOCKY / FOLDED | GSI 60 | GSI 50 | GSI 40 | GSI 30 | GSI 20
CRUSHED (Poorly interlocked) | GSI 50 | GSI 40 | GSI 30 | GSI 20 | GSI 10
MODULE 6 • RECONSTRUCTED VISUAL MATRIX
Geological Strength Index () Contour Chart
Always estimate a RANGE of GSI values (e.g., GSI 45–55) rather than a single discrete integer to account for field spatial variability.

## Slide 42
MODULE 6 • MATHEMATICAL QUANTIFICATION
Quantification of GSI: Block Volume () & Joint Condition ()
components: (large scale undulation), (small scale asperities), (mineral weathering).
To eliminate subjective observer bias, Cai et al. (2004) quantified GSI's two axes using measurable field parameters: Block Volume () and Joint Condition Factor ().
Quantitative Chart Placement
Calculating () gives the precise ordinate on the vertical axis.
Calculating gives the precise abscissa on the horizontal axis. Intersection pinpoints exact objective GSI value.
Joint Condition Factor ()
Where = Waviness (), = Smoothness (), = Alteration ().
Persistent Block Volume ()
Where = joint set spacing (), = angles between joint sets.

## Slide 43
MODULE 6 • COMPLEX GEOLOGIES
Extending GSI to Complex & Heterogeneous Flysch
Flysch complexity: Sandstone beds provide structural skeleton while clay/shale matrix controls continuous squeeze deformations.
Tectonically sheared, interbedded sandstone-siltstone-shale sequences (Flysch / Athens Schist) lack distinct continuous joint sets, rendering standard blocky GSI charts unusable.
Weighted Matrix Approach
The composite rock mass strength is calculated by weighting the volumetric proportions of strong sandstone beds () versus weak sheared shale matrix ().
Prevents extreme over-design in complex alpine flysch tunnels.
Hoek & Marinos (2000) Special Categories
•
Sub-category A: Intact interbedded sandstone/siltstone beds.
•
Sub-category B: Folded sandstone beds with minor shearing.
•
Sub-category C: Heavily sheared siltstone containing broken sandstone fragments.
•
Sub-category D: Tectonically crushed clayey matrix with isolated sandstone lenses.

## Slide 44
MODULE 6 • CONSTITUTIVE MECHANICS
Linking GSI to Non-Linear Hoek-Brown Criterion
GSI scales intact rock parameter down to, and intact cohesion down to . accounts for blast stress damage.
DISTURBANCE FACTOR D
Blast Damage Factor ()
for un-disturbed TBM excavations or controlled smooth blasting.
for severe blast damage in bench blasting or poor production shooting.
= Frictional rock mass material constant:
= Cohesive rock mass tensile strength constant:
= Curvature exponent constant ( for ):

## Slide 45
MODULE 6 • SYSTEM LIMITS
Limitations & Correct Application of GSI
1. DO NOT Use for Structurally Controlled Wedge Falls
When excavation stability is governed by 1 or 2 dominant intersecting joint sets forming discrete wedges, use kinematic stereonet analysis and UNWEDGE software, NOT GSI.
2. Assumes Isotropic Homogeneous Media
GSI assumes the rock mass contains sufficient randomly oriented joint sets (3+ sets) that it can be treated as an equivalent isotropic continuum.
3. Inapplicable to Deep Hard Rock Bursting
Brittle strain-bursting and face spalling in deep massive hard rock under extreme stress () cannot be predicted by GSI.
4. Yields NO Support Recommendations
GSI does NOT provide empirical tables for shotcrete thickness or bolt spacing (unlike RMR/Q). Support sizing must be calculated via numerical FEA simulation.
Notes: We now compare all major systems and establish an integrated geotechnical design workflow.

## Slide 46
MODULE 7 • SECONDARY SYSTEMS
Alternative European Systems: & Rock Mass Number ()
Useful secondary systems in European TBM tunneling and squeezing rock evaluations.
Quantifies uniaxial compressive strength of the rock mass based on intact strength () scaled by a Jointing Parameter (). Used heavily in TBM performance modeling.
Defines a stress-free Q-index (). Eliminates difficulty in estimating in deep tunneling for squeezing assessment.
PALMSTRÖM (1995)
Rock Mass Index ()
STRESS-FREE INDEX
Rock Mass Number ()

## Slide 47
MODULE 7 • SYSTEM CROSS-CORRELATIONS
Empirical Correlations Between , , and
Correlations provide useful sanity checks, but field data must be collected separately for both systems.
Correlation Warning
Scatter across conversion equations can exceed rating points.
NEVER rely solely on converted ratings for final support design. Always map parameters independently in the field.
Bieniawski (1976) Correlation (111 Tunnel Case Histories)
Abad et al. (1983) Correlation (187 Coal Mining Cases)
Hoek, Kaiser & Bawden (1995) GSI Correlation (for , Dry)

## Slide 48
System | Primary Parameters | Main Application | Key Output / Output Type | Major Limitation
Terzaghi (1946) | Qualitative rock block description | Rail tunnels with steel arches | Rock load factor (Steel set sizing) | Overestimates support for ; no bolts/shotcrete
RQD (1967) | Core piece lengths % | Core logging, general indexing | Rock mass quality % score | Directional borehole bias; ignores joint surface condition
RSR (1972) | Geology, Geometry, Water + Joints | Small steel/shotcrete tunnels | Numerical score 0-100 () | Based on small tunnel database; uses Imperial units
RMR (1973/89) | , , Spacing, Condition, Water, Dip | Tunnels, mines, slopes () | Stand-up time, support table, | Conservative no-support limit; inaccurate in weak rock
Q-System (1974/02) |  | Tunnels, caverns, mines | Support map ( vs ), bolt length, | difficult to select; open log scale hard to use
GSI (1994/06) | Block interlocking vs Surface quality | Weak/jointed rock, numerical FEA | Hoek-Brown constitutive parameters () | No support tables; unusable for discrete joint wedges
System | Primary Parameters | Main Application | Key Output / Output Type | Major Limitation
Terzaghi (1946) | Qualitative rock block description | Rail tunnels with steel arches |  | 
RQD (1967) |  | Core logging, general indexing | Rock mass quality % score | Directional borehole bias; ignores joint surface condition
RSR (1972) | Geology, Geometry, Water + Joints | Small steel/shotcrete tunnels |  | Based on small tunnel database; uses Imperial units
RMR (1973/89) |  |  |  | Conservative no-support limit; inaccurate in weak rock
Q-System (1974/02) |  | Tunnels, caverns, mines |  | 
GSI (1994/06) | Block interlocking vs Surface quality | Weak/jointed rock, numerical FEA |  | No support tables; unusable for discrete joint wedges
MODULE 7 • SYSTEM SYNTHESIS
Systematic Comparison Matrix of Major Systems

## Slide 49
MODULE 7 • PRACTICAL ENGINEERING WORKFLOW
Integrated Engineering Design Pipeline
Empirical classification guides initial support installation, but field monitoring (Observational Method) confirms safety during excavation.
1
Geological Mapping & Core Logging: Measure intact UCS (), log RQD, joint set count (), spacing, roughness (), alteration (), and water inflow.
2
Calculate Empirical Ratings: Independently compute , -index, and select visual range. Cross-check for inconsistencies.
3
Empirical Support Selection: Sizing primary temporary support (rock bolt pattern, SFRS shotcrete thickness) using Barton chart and RMR tables.
4
Kinematic Stability Analysis: Perform stereonet projection (UNWEDGE / DIPS) to verify roof and sidewall structural wedge fall safety.
5
Numerical Simulation (FEA / FLAC): Input , , and Hoek-Brown into 2D/3D numerical engines to verify tunnel plastic zones and convergence.
6
Observational Method & Instrumentation: Monitor real-time tunnel convergence with optical targets and MPBX extensometers to adjust support in field.

## Slide 50
Summary & Core Takeaways
1. Engineering Aids, Not Cookbooks Classifications guide empirical design—they never replace analytical, kinematic, or numerical field monitoring studies.
2. Always Cross-Check Systems Apply at least TWO independent classification systems (e.g., RMR and Q) on every geotechnical project.
3. Direct Mechanics Mapping RMR yields ; Q yields support maps ( vs ); GSI yields non-linear Hoek-Brown numerical inputs ().
4. Respect System Boundaries Do NOT use GSI for wedge falls; do NOT use RMR for squeezing rock; do NOT use Terzaghi for rock bolts.
Questions & Discussion